## Slide 1: ECE411 Final Project Efficient Pipelined RISC-V Processor
ZJU-UIUC Institute
Ziyuan Chen
Zhirong Chen
Hao Ren

## Slide 2
CP1

## Slide 3
CP2

## Slide 4: Advanced Feature Design

## Slide 5
CP3

## Slide 6: Branch Predictor & Branch Target Buffer
Global Branch Predictor
Local Branch Predictor
Branch Target Buffer

## Slide 7: Cacheline Prefetcher
Performance is poor because……
  there are too many cache hits, and
  blocking cache & 1 sets of memory ports

## Slide 8: Parameterizable Cache
Generalized PLRU (custom #sets, #ways)
PLRU[s][{2'b01, WAYHIT} >> (i+1)]
<= WAYHIT[i];
Update at way #3: XX1XX10
PLRU[s][3'b101] <= 1'b1;
PLRU[s][3'b010] <= 1'b1;
PLRU[s][3'b001] <= 1'b0;
Update at way #6: 0XXX1X1
PLRU[s][3'b111] <= 1'b0;
PLRU[s][3'b011] <= 1'b1;
PLRU[s][3'b001] <= 1'b1;
Way #3 is LRU: ??0??01
if (PLRU[addr_index][3'b101] == 1'b0 &
PLRU[addr_index][3'b010] == 1'b0 &
PLRU[addr_index][3'b001] == 1'b1 )
Way #6 is LRU: 1???0?0
if (PLRU[addr_index][3'b111] == 1'b1 &
PLRU[addr_index][3'b011] == 1'b0 &
PLRU[addr_index][3'b001] == 1'b0 )
PLRU_signals[m] &=
(PLRU[addr_index][{2'b01, w} >> (i+1)]
!= w[i]);
Did we miss some edge cases?

## Slide 9: Parameterizable Cache
Customizable Word Size
  In bus adaptor
    assign mem_wdata_l = {(s_word/32){mem_wdata}};
    assign mem_rdata = mem_rdata_l[(32*address[s_offset-1:2]) +: 32];
    assign mem_mask_l = {{(s_mask-4){1'b0}}, mem_mask} << (address[s_offset-1:2]*4);
  In cacheline adaptor
    READ:
    if (counter == n_burst - 1)
    next_state = DONE;
    WRITE:
    burst_o = line_i[counter*64 +: 64];
    if (counter == n_burst - 1)
    next_state = DONE;
if (state == DONE)​
counter <= 0;​
else if (resp_i)​
buffer <= {burst_i, buffer[s_word-1:64]};​
counter <= counter + 1;
Don't forget the bmem burst size!
But this comes with side effects.

## Slide 10: Unique Challenges We Have Faced
Coremark is weaker than autograder tests
  There are no LUI instructions
  And it has bugs!
Most advanced design drags performance down
  E.g., is the prefetcher working?
Area was once huge
  Registered cache didn't turn out well
Configuring the param'able cache
  Recompiling SRAM (.db)
  PLRU fails when #ways = 1 (?!)

## Slide 11: Statistics

## Slide 12: Statistics

## Slide 13
Constraints (Experiments use a less optimized commit)
  L1 cache: fixed at 16 sets, 4 ways (MP3, MP4CP2)
  L2 cache: 128KB budget
Tradeoffs
  Smaller word size, lower miss penalty
  Larger word size, lower miss rate only for instruction cache (why?)
Statistics
Optimizing Cache
s_word | #sets | #ways | Exec time | IPC | L1 Instr Cache |  | L1 Data Cache |  | L2 Instr Cache |  | L2 Data Cache | 
 |  |  |  |  | Hit/Miss | Penalty | Hit/Miss | Penalty | Hit/Miss | Penalty | Hit/Miss | Penalty
256 | 0 | 0 | 32524050000 | 0.229373 | 1173571/1280 | 11.059 | 73801/135 | 14.667 |  |  |  | 
128 | 64 | 16 | 32776490000 | 0.227675 | 1173862/8476 | 5.610 | 7740/736 | 9.029 | 73361/575 | 8.647 | 784/171 | 9.819
256 | 128 | 4 | 32477390000 | 0.229732 | 1173378/1280 | 7.684 | 900/380 | 11.045 | 73801/135 | 12.289 | 106/87 | 11.977
512 | 16 32 | 16 8 | 33299490000 | 0.223949 | 1259468/505 | 10.194 | 305/200 | 15.120 | 73890/46 | 18.717 | 2/45 | 15.978
1024 | 16 32 | 8 4 | 33378390000 | 0.223395 | 1269162/139 | 20.568 | 36/103 | 23.019 | 73912/24 | 27.375 | 0/24 | 24.375
Sadly, we were forced to go with
s_word = 128, #sets = 16, #ways = 1
to meet the 75000 area constraint

## Slide 14: Looking Back, We Would Rather……
Start earlier
  We basically missed all deadlines
  It accumulates!
Design the pipeline differently
  Moving from the FSM approach
  It involves way too many dependencies